## Slide 1: RNA and DNA library prep for mNGS
Rapid Response – Revised 01/12/2026

## Slide 2: mNGS pipeline
Study design
xNA extraction
Library prep
Sequencing
Data analysis
Type(s)
Controls
Storage
Lab setup
Type(s)
Controls
QC
Host removal
Fragmentation
dsDNA generation
End-repair
Adapter ligation
Barcoding & PCR
Clean-up
Pooling
QC
QC data
Host removal
Alignment
Blast
Ranking of hits
Machine
Read length
Loading conc.
Pathogen ID

## Slide 3: Library prep: RNA to sequencing library
Sequencing library = Pool of DNA inserts with sequencing adapters attached
Extracted RNA
Sequencing library

## Slide 4: Steps in library preparation:
1. Host depletion, RNA fragmentation + priming
2. First strand cDNA synthesis
3. Second strand cDNA synthesis
4. End Prep
5. Adapter Ligation
6.. USER + Barcoding PCR

## Slide 5: Library prep
Sequencing library = Pool of DNA inserts with sequencing adapters attached

## Slide 6: Library prep
F
L
O
W
C
E
L
L
Sequencing process:
Read 1
F
L
O
W
C
E
L
L
Read 2
Notes: Animation shows how your library is sequenced.

## Slide 7: Library prep
RNA or DNA library
Notes: RNA and DNA library prep steps. We’ll go into detail of RNA library prep since that is the more complicated one. And once you are familiar with RNA library prep, you’ll find DNA library prep to very similar but simpler.

## Slide 8: RNA library prep
STEP 0. Starting material: RNA or TNA
RNA only: move on to host rRNA depletion
TNA (total nucleic acid): need to remove DNA
  Aliquot sample
  DNAse I treatment
  SPRI bead clean-up (2x)
  Qubit quantification
Notes: If you extract RNA you can proceed to the next step. But if you extracted total nucleic acid, you’ll have to remove the DNA first. This can be achieved by DNAse I treatment

## Slide 9: RNA library prep
STEP 1. Host rRNA depletion
Before RNA extraction:
  Serum or plasma instead of blood
  Supernatant of CSF to remove WBCs
Human RNA depletion kits to use after RNA extraction:
  TruSeq Stranded total RNA Human (previously Ribo-Zero, Illumina)
    Biotinylated, target-specific oligos + Ribo-Zero beads to fish out rRNA
  FastSelect (Qiagen): $150 for 24 samples when reagent is diluted 1:10
    Proprietary technology, presumably with hybridizing probes that make rRNA inaccessible to enzymes in subsequent steps
RNA content of typical host sample
95% host rRNA
2-3% host mRNA
1% other host RNA
<1% pathogen RNA
Preferred
(no extra wash required)
Notes: Next step involves removing as much human host material as possible. The RNA content of a typical host sample will be 95% host rRNA, 2-3% host mRNA and 1% other host RNA. And then less than 1% usually is pathogen RNA. If you prepare a sequencing library from such a sample, all of these types of RNA would be sequenced, and only 1% of your reads would be from pathogens that you are interested in. So it’s important to first remove host rRNA as much as possible, to allow your pathogens take up more of the sequencing data.
FastSelect takes host rRNA from 95% to about 30% in our hands

## Slide 10: RNA library prep
STEP 2. Fragmentation
Ideal insert size = ± 400 nt
Several ways to fragment RNA:
  Enzymatic: %GC-dependent -> may bias mNGS results
  Heat cycling: relatively random
  Sonication: larger volume required, expensive machine, contamination risk
  Divalent cations: allow RNA to be self-cleaving (Mg2+, Ca2+, Zn2+, …)
    Mg2+ and heat (94oC) for 2-15 minutes depending on RNA quality
      High quality RNA: long fragmentation time
      Low quality RNA: short fragmentation time
Fragmentation
± 400 nt
± 400 nt
± 400 nt
NEBNext Ultra ii RNA library kit
Notes: FastSelect takes host rRNA from 95% to about 30% in our hands

## Slide 11: RNA library prep
STEP 2. Fragmentation
Fragmentation pattern of high quality RNA
Use shorter fragmentation times when RNA quality is compromised!
Notes: From NEBNext Ultra II RNA First Strand Synthesis Module E7771 manual

## Slide 12: RNA library prep
STEP 3. dsDNA synthesis
First strand synthesis
Second strand synthesis
Purify dsDNA by SPRI bead clean-up (1.8x)

## Slide 13: RNA library prep
STEP 4. End repair & dA-tailing
Remove overhangs to get blunt ends
Prep fragment to clone on adapters
  Add 5’ phosphate (T4 kinase)
  Add single 3’ A overhang to clone on adapters
(T4 DNA polymerase)
  Note: After end-repair, move on to adapter ligation step ASAP
  (5’ phosphate is fragile)

## Slide 14: RNA library prep
STEP 5. Adapter ligation
Adapters are added to allow sequencing
Remove adapter dimers by SPRI bead clean-up (0.9x)
  Adapter dimers are our enemy #1 after this step (short fragments get preferentially sequenced)

## Slide 15: RNA library prep
STEP 6.
USER digestion & barcoding PCR
USER enzyme opens up adapters
i5 and i7 oligos are added by PCR
SPRI bead clean-up (0.8x)
...
Notes: Reduce #PCR cycles to the absolute minimum to avoid amplification bias.

## Slide 16: RNA library prep
Final library for one sample

## Slide 17: RNA library prep
How to prepare
a library in the lab?

## Slide 18
1 rxn,
fragm. by Mg2+ & heat
1 rxn for 1st str. synt.
1 rxn for 2nd str. synt.
1 rxn
1 rxn, U shaped adapters
1 rxn
NEBNext
Ultra II RNA
Illumina
Nextera
Illumina
TruSeq
1 rxn,
fragm. by Mg2+ & heat
1 rxn for 1st str. synt.
1 rxn for 2nd str. synt.
1 rxn
1 rxn, Y shaped adapters
1 rxn
1 rxn,
Transposome frag. and ligation of adapters
1 rxn
cDNA made separately
RNA library kit options
Notes: We’ll use the NEBNextUltra II RNA kit as an example

## Slide 19: RNA library prep (NEBnext Ultra II RNA)
RNA fragmentation, priming and host rRNA removal
Prepare mix
Reagents | μl per reaction
RNA sample (10ng – 100ng total) | 4
First Strand Synthesis Reaction Buffer (5x) | 4
Random Primers | 1
*QIAseq FastSelect (1:100) rRNA | 1
Total volume | 10
2. Thermocycler:
2-8 min at 94oC: fragmentation
2 min at 75oC
2 min at 70oC
2 min at 65oC
2 min at 60oC
2 min at 55oC
5 min at 37oC
5 min at 25oC
Hold at 4oC
Slow ramp for FastSelect to specifically anneal to host rRNA
Time depends on RNA quality!
All in pre-PCR lab
Notes: Removed ERCCs here

## Slide 20: RNA library prep
B. First Strand Synthesis
Prepare mix
Reagents | μl per reaction
Fragmented and primed RNA | 10
Nuclease-free water | 8
NEBNext First Strand Synthesis Enzyme Mix | 2
Total volume | 20
2. Thermocycler:
10 min at 25oC: random primer annealing
15 min at 42oC: reverse transcription rxn
15 min at 70oC: heat inactivation of enzymes
Hold at 4oC
All in pre-PCR lab
Notes: Random primers are about 5 bp long, so low annealing temperature of 25C

## Slide 21: RNA library prep
C. Second Strand Synthesis
Prepare mix
Reagents | μl per reaction
First strand synthesized DNA | 20
2nd Strand Synthesis Reaction Buffer (10x) | 8
2nd Strand Synthesis Enzyme Mix | 4
Nuclease-free water | 48
Total volume | 80
2. Thermocycler (HEATED LID OFF):
1 hr at 16oC: 2nd strand synthesis
Hold at 4oC
3. SPRI bead cleanup (1.8x) to purify dsDNA
All in pre-PCR lab
Notes: RNAseH knicks RNA strand
DNA polymerase produces second strand
DNA ligase fills up the gaps

## Slide 22: RNA library prep
D. End prep of cDNA
Prepare mix
Reagents | μl per reaction
Purified dsDNA | 50
Ultra II End Prep Reaction Buffer (8.6x) | 7
Ultra II End Prep Enzyme Mix | 3
Total volume | 60
2. Thermocycler (heated lid at 105oC):
30 min at 20oC:
Klenow fragment creates blunt ends
T4 kinase adds 5’ phosphate,
T4 DNA polymerase adds 3’ A overhang
30 min at 65oC: heat inactivation of enzymes
Hold at 4oC
3. Proceed immediately to next step, do NOT freeze.
All in pre-PCR lab
Notes: Enzymes: Klenow fragment to get blunt ends
T4 polynucleotide kinase to add 5’ phosphate
T4 DNA polymerase to add 3’ A overhang

## Slide 23: RNA library prep
E. Adapter ligation
Prepare mix
Reagents | μl per reaction
End prep reaction mixture | 60
NEBNext Ultra II Ligation Master Mix | 30
NEBNext Ligation Enhancer | 1
1:10 Adapters (only add at the very end, do not pre-mix) | 2.5
Total volume | 93.5
2. Thermocycler (HEATED LID OFF):
15 min at 20oC
3. Proceed immediately to SPRI bead cleanup (0.9x)
All in pre-PCR lab
Notes: Enhancer: likely DMSO, acts as crowding agent
Add adapters only at the very end to avoid adapter dimers forming in the mix.

## Slide 24: RNA library prep
F. USER digestion and Barcoding PCR
Prepare mix
Reagents | μl per reaction
Purified, adapter-ligated dsDNA | 15
USER Enzyme | 3
NEBNext Ultra II Q5 Master Mix | 25
5 μM i7 barcoded primer | 5
5 μM i5 barcoded primer | 5
Total volume | 53
2. Bring tubes/plate to POST-PCR lab
3. Thermocycler (Heated lid at 105oC):
15 min at 37oC: USER enzyme activity
30 sec at 98oC
10 sec at 98oC
75 sec at 65oC
5 min at 65oC
Hold at 4oC
6 to 15 cycles
4. SPRI bead cleanup to remove amplified dimers
Post-PCR lab
Pre-PCR lab
Notes: Enhancer: likely DMSO, acts as crowding agent
Add adapters only at the very end to avoid adapter dimers forming in the mix.

## Slide 25
1 rxn,
fragm. by Mg2+ & heat
1 rxn for 1st str. synt.
1 rxn for 2nd str. synt.
1 rxn
1 rxn, U shaped adapters
1 rxn
NEBNext
Ultra II RNA
Illumina
Nextera
Illumina
TruSeq
1 rxn,
fragm. by Mg2+ & heat
1 rxn for 1st str. synt.
1 rxn for 2nd str. synt.
1 rxn
1 rxn, Y shaped adapters
1 rxn
1 rxn,
Transposome frag. and ligation of adapters
1 rxn
cDNA made separately

## Slide 26: DNA library prep
gDNA or cDNA
Fragmentation
NEBNext
Ultra II FS DNA
Illumina
Nextera XT
(small genomes, cDNA, amplicons)
Illumina
DNA Prep
WGS, cDNA, amplicons
1 rxn,
Fragm. enzyme + repair enzymes
1 rxn, U shaped adapters
1 rxn
1 rxn
1 rxn,
Transposome frag. + ligation on bead
1 rxn,
Transposome frag. + ligation in solution
1 rxn
DNA library kit options
Notes: DNA library prep follows the same steps as RNA library prep, except that the RT step is not required and that fragmentation happens enzymatically or by a transposome (instead of Mg2+ and heat for RNA library prep)

## Slide 27: Library prep QC
Dimers (143 bp)
Dimers
Library
Library (250-1000 bp)
Library QC: quantity & quality
Quantity (ng/μl): Qubit to determine concentration of individual libraries (0.5-10 ng/μl)
Quality (bp): Tapestation to determine (i) length of library and (ii) degree of dimers present
Post-PCR lab

## Slide 28: Library prep QC
3 rounds
SPRI (0.85x)
After PCR amplification
After SPRI bead clean-up
Library QC: quantity & quality
Quantity (ng/μl): Qubit to determine concentration of individual libraries (0.5-10 ng/μl)
Quality (bp): Tapestation to determine (i) length of library and (ii) degree of dimers present
Size selection by SPRI beads
to remove dimers
ALL DIMERS SHOULD BE REMOVED!
Adapter dimers
Post-PCR lab
Notes: Adapter dimers are short fragments and since short fragments are preferentially sequenced, even a relatively small amount of adapter dimers in your library will cause adapter sequences to take up a large proportion of your sequencing data. Avoid this waste of sequencing data by removing all adapter dimers from your library prior to loading the sequencer!
If no tapestation then do diagnostic PCR: take 1 ul library and use Illumina universal primers to PCR (35-40 cycles) and run on a gel. If dimers seen -> SPRI more
Tapestation and QPCR for quantification: ideal size is 550 nt, but anything between 200-1000 is ok.

## Slide 29: Library prep QC
AMPure XP SPRI select beads (paramagnetic)
or homemade SPRI beads (>10x cheaper)
The longer a fragment, the better it will bind to the beads
The fewer beads you add, the more short fragments you’ll lose
Perform size selection using SPRI beads to remove adapter dimers (143 bp)
Volume beads
Volume reaction
SPRI ratio =
Example: for a 1.8x SPRI clean-up:
Add 18 μl of SPRI beads to 10 μl of sample
Notes: Buffer is PEG (crowding), NaCl (precipitation), Tween (reduce plastic stickiness) and TE buffer.

## Slide 30: Library prep QC
Step | Ideal RNA/library size | To remove | SPRI ratio
After DNAse I treatment | - | Reagents | 
After second strand synth. | ± 400 bp | Reagents | 1.8x
After adapter ligation | ± 464 bp | Adapter dimers (64 bp) & reagents | 0.9x
After P7/P5 PCR | ± 543 bp | P5-adapter dimer-P7 (143 bp) & reagents | 0.8x
QC of library | ± 543 bp | P5-Adapter dimer-P7 (143 bp) | 0.8x
SPRI bead clean-ups during library prep
Size selection using SPRI beads to remove adapter dimers
Rule of thumb: dimers should be completely should disappear before
Notes: Adapter dimers should be less than 1% of your total library
P7: 24 nt p7 + 12 nt barcode + 2 nt + 32 nt adapter compl.
P5: 20 nt p5 + 9 nt +12 nt barcode + 33 nt adapter compl.

## Slide 31: Library prep QC
Final QC & seq prep
Pooling samples for sequencing
Each sample has a unique set of barcodes -> multiple samples can be pooled in one sequencing reaction
QCed Sample A
QCed
Sample B
QCed
Water control A
Pool
BC2
BC1
BC3
BC4
BC5
BC6
Notes: Every sample has its own set of barcodes, so everything can be pooled.

## Slide 32: Library prep QC
Pooling samples together for sequencing
  Qubit to determine concentration of individual libraries (expect library to be 0.5 to 10 ng/ul)
  Pool barcoded libraries so that all are equally represented (except H2O controls, only 1:5)
Sample 1: 10 ng/ul -> 4.0 μl -> 40 ng
Sample 2: 5 ng/ul -> 8.0 μl -> 40 ng
Sample 3: 8 ng/ul -> 5.0 μl -> 40 ng
Sample 4: 15 ng/ul -> 2.6 μl -> 40 ng
H2O control: 1 ng/ul -> 8.0 μl -> 8 ng
End goal is >10 μl of 2 nM pooled library (or 4 nM for MiSeq)
Qubit concentration
Pool
168 ng
Total: 27.6 μl
Notes: 10 ng/ul would be a lot for a library -> tone down PCR cycles next time

## Slide 33: Library prep QC
Pooling samples together for sequencing
3. After pooling, determine quantity and quality of pool
concentration in ng/μl
660g/mol x average library size in bp
x 106
Qubit
Concentration in nM =
Capillary or gel electrophoresis
Example: if concentration is 6.1 ng/μl, and average library size is 550 bp -> concentration is 16.8 nM
Pick one way to calculate nM and stick with it!
Qubit concentration and library size
Automatic calculation by Tapestation
End goal is >10 μl of 2 nM pooled library

## Slide 34: Library prep QC
Pooling samples together for sequencing
3. After pooling, determine quantity and quality of pool
Or use Tapestation to calculate concentration of library in nM for fragments between 200-1000 bp long
(see extra slides for a step-by-step guide on how to set that up)
200-1000 bp: 9.92 nM
Pick one way to calculate nM and stick with it!
Qubit concentration and library size
Automatic calculation by Tapestation

## Slide 35: Library prep - preparing to load the sequencer
Dilute library to the correct loading concentration:
  iSeq:
    dilute to 75 pM (or another optimized concentration),
    Spike in 1-5% of PhiX at the same concentration
  MiSeq:
    First denature library with sodium hydroxide (NaOH)
    Then dilute to 10-12 pM (or another optimized concentration)
    Spike in 1-5% of denatured PhiX to denatured and diluted library
See slide decks for iSeq or MiSeq loading for more details!

## Slide 36
Next step:
iSeq or MiSeq loading